## Slide 1: Breaking Down Barriers: Seamless Protocol Conversion with UVM Component Layering
Santosh Mahale , Shantanu Lele
Sr. Staff Engineer , Marvell Technologies , Pune

## Slide 2: Agenda
Introduction
Problem statement
Proposed solution
Layering architecture
Case Study
Results

## Slide 3: Introduction
Increasing computing needs and maturing technology changes demands change in how various blocks in System on chip (SoC) are connected.
Over the time as architecture evolves ; processor native buses upgrades to newer protocols for better performance.
Even through there are no significant change in various IP’s ; change in native processor bus results into change in IP interfaces for compatibility and to optimize the performance.
Whether scope of RTL change is minimum or widespread, DV infrastructure needs significant change to meet even initial milestones; creating bottleneck in project timeline.

## Slide 4: Problem statement
Interconnect
CPU
Hardware
Accelerator
Egress IP
Ingress IP
MMU
Memory
Protocol convertor

## Slide 5
MESH
Protocol convertor
Legacy IP
Protocol A
Protocol B
Subsystem

## Slide 6: What are the options ?
Verify subsystem without protocol converter. increased risk of finding integration bugs at full chip.
1
2
3
Start verification with legacy IP only and later add bridge in subsystem testbench. Redundant work on legacy interface.
Use layering component which will allow developing verification collaterals such as tests & sequences on new interface right away.

## Slide 7: Proposed solution
M
E
S
H
VIP A
A2B
Layering component
VIP B
Legacy IP
Protocol convertor
tests
- Main component
- Layering component

## Slide 8: Layering architecture
Protocol response convertor(De-Layering)
Protocol request convertor (layering)
Sequencer
Driver
Monitor
Monitor
Driver (unused)
Sequencer
Protocol A sequences

## Slide 9
Driver B
Sequencer B
Sequencer A
Driver A
(1) get_next_item()
Choose a transaction to be executed
Acknowledge the sequence
Acknowledge the sequence
(1) Start_item()
(2) Randomize seq A
(2A) Convert sequence A to sequence B
(2B) Start A2B conv_seq on sequencer B
(3) Deliver transaction to driver B
(4) Send item to DUT
(4a) Collect response()
Item_done()
Route resp back to original seqeunce
Convert and route resp back to original sequence
(4b) get_response()

## Slide 10: Case study
Subsystem base test
CHI Sequence
mon
drv
CHI Seqr
AXI Seqr
chi2axi req conversion
axi2chi resp conversion
AXI Seq
mon
drv
Subsystem env
CHI A
AXI Seqr
CHI VIP
AXI VIP

## Slide 11: Results

## Slide 13: Relevance
1
Reusable verification component.
2
Left shift verification cycle, providing opportunity to stress various scenarios at Sub-system level TB.
3
Generic architecture can be extended to do conversion from
any to any bus protocol.

## Slide 14: References
[1] Accellera, “UVM User Guide, v1.1d”, www.uvmworld.org
[2] Accellera, “UVM Reference Guide, v1.1d”, www.uvmworld.org

## Slide 15: Acknowledgement
We profoundly thank colleagues and management team at Marvell Technologies, India for their valuable support
Thanks to DVCON INDIA for giving us this opportunity

## Slide 16: Questions